## Slide 1: Tracked Robot Design
Nathan Lucas
CARES Lab
Wayne State University

## Slide 2: Outline
Hardware Design
Hardware Installation
Software
Software Build Guide
Backup

## Slide 3: Hardware Design

## Slide 4: Components
6700 mAh
Li-ion
Tracked Robot
DRV8835
Dual Motor
Driver Kit
Dagu Rover 5
Tracked Chassis
Raspberry Pi 2 Model B
Edimax
EW-7811Un
USB Wi-Fi
Module
Platform
Controller
Power
Wireless
Motor Driver
IEEE
802.11
GPIO
3.3V power
PWM signals
5V power
USB
100 mA
USB LED
Lamp
5200 mAh
Li-ion
16 GB
microSDHC

## Slide 5: Motor Driver
Pololu DRV8835 Dual Motor Driver Kit for Raspberry Pi
  DRV8835 dual H-bridge motor driver
  FET for reverse battery protection
  GPIO header
  Optionally power Raspberry Pi through add-on regulator (not included)
  https://www.pololu.com/product/2753
Python library
  https://github.com/pololu/drv8835-motor-driver-rpi
Alternative
  MC33926 motor driver board if higher current is needed
Parameter |  | Value | 
Supply voltage | Minimum | 1.5 | V
 | Maximum | 11 | V
Current (per channel) | Continuous | 1.2 | A
 | Max peak | 1.5 | A
PWM frequency | Maximum | 250 | kHz

## Slide 6: Power and Motor Control Concept
Li-ion Battery (×2)
Raspberry Pi 2B
Motor 2
Motor 1
DRV8835 Dual
Motor Driver

## Slide 7: Power and Motor Control
GPIO
DRV8835 Motor Driver Kit for Raspberry Pi
Motor 1
Motor 2
5.1 Ah
Li-ion
Battery
Pack
~5V
–
+
VOUT
5V
1
3
2
GND
M1A
M1B
M2A
M2B
4
3
2
1
VIN
GND
2
1
5V
GND
2
4
6
9
14
20
25
30
34
3V3
17
2
3
4
5
13
6
DRV8835 Dual Low
Voltage H-Bridge IC
VM
AOUT1
AOUT2
BOUT1
BOUT2
VCC
GND
GND
12
1
2.7-11.8V
5V
M2DIR
M1DIR
M2PWM
M1PWM
29
31
32
33
GPIO6
GPIO5
GPIO13
GPIO12
10
8
9
7
Reverse Polarity
Protection
Voltage Regulator Interface
(Not Used)
LED Lamp
Toggle
Switch

## Slide 8: Motor Driver Interface
M2PWM
M2DIR
M1DIR
M1PWM
5V
VCC
3V3
GPIO2
GPIO3
GPIO4
GND
GPIO17
GPIO27
GPIO22
3V3
GPIO10
GPIO9
GPIO11
GND
GPIO0
GPIO5
GPIO6
GPIO13
GPIO19
GPIO26
GND
5V
5V
GND
GPIO14
GPIO15
GPIO18
GND
GPIO23
GPIO24
GND
GPIO25
GPIO8
GPIO7
GPIO1
GND
GPIO12
GND
GPIO16
GPIO20
GPIO21
1
3
5
7
9
11
13
15
17
19
21
23
25
27
29
31
33
35
37
39
2
4
6
8
10
12
14
16
18
20
22
24
26
28
30
32
34
36
38
40
J8
Raspberry Pi
GPIO
+3V
Motor 1 Direction
Motor 2 Direction
Motor 2 PWM
Motor 1 PWM
+5V
Not Used

## Slide 9: Motor Driver Interface
26 AWG
20 AWG
20 AWG
20 AWG
20 AWG
26 AWG
1
Housing
TE P/N
1744036-4
Housing
TE P/N
1744036-2
Header
TE P/N
1744048-2
Header
TE P/N
1744048-4
1
Li-ion
Battery
+
–
Motor 1
(Left)
Motor 2
(Right)
2.54 mm (0.100 in) Pitch
5.08 mm (0.2 in) Pitch
DRV8835 Motor
Driver Kit for
Raspberry Pi
3×1 Socket Strip
Voltage Regulator
Interface (Not Used)

## Slide 10: ...
GPIO Header
Motor Driver
Controller Standoff
Hex Nut
Hex Nut
Battery Power
Motor Power

## Slide 11: Hardware Installation

## Slide 12: Wiring Connectors
Motor 2
Motor 1
TOP
Extract contacts
and reuse in motor
connector housing
Do NOT cut wires
FORWARD

## Slide 13: Wiring Connectors
Motor 2
Motor 1
1
1
Note opposite
polarities
of motors
Toggle
switch
USB Micro-B
receptacle
USB A
plug
USB A
receptacle
USB cable
FORWARD
5
1
4
1

## Slide 14: Mounting Holes
Motor 1
Motor 2
1
FRONT
TOP
Tap #6-32 UNC (×4)
FORWARD

## Slide 15: Controller Mount
Raspberry Pi 2B
TOP
56
85
58
49
FRONT

## Slide 16: Controller Mount
TOP
Controller Mounting Plate
203×127 mm (8×5 in)
FRONT
Polycarbonate Sheet
203×254 mm (8×10 in)
(Makes 2 Mounting Plates)
USB
Cut slot for
Motor Cable
Cut slot for
Toggle Switch
Drill holes for
USB Micro-B
Breakout Board
RPi 2B
GPIO Header
Drill holes to
Mount Controller
Drill holes
for attaching
Controller Mount
to Chassis

## Slide 17: Controller Mounting Plate
TOP
⌀ ?/? in (×4)
⌀ ?/? in (×2)
⌀ ?/? in (×5)
8 in
5 in
? in
? in
Use USB Micro-B
breakout board
as a template for
marking holes
? in

## Slide 18: Controller Mounting Plate
TOP
⌀ ?/? in (×4)
⌀ ?/? in
?
Use Raspberry Pi board as
a template for marking holes
?
? in
? in

## Slide 19: Controller Mount
TOP
Standoff, 6-32 × 1.5-in, Aluminum (×4)
Standoff, M2.5-0.45 × 6 mm, Nylon (×4)
under plate: Nut, M2.5-0.45, Nylon (×4)
FRONT
RPi 2B
GPIO Header

## Slide 20: Controller Mount
TOP
Attach Controller with M2.5 Nylon Screws (×4)
FRONT

## Slide 21: Motors and Power
Motor 2
Motor 1
Toggle
switch
Micro-B
receptacle
A plug
USB A
receptacle
USB cable
Micro-B
plug
USB cable
A plug
Micro-B
plug
5
1
LED
lamp

## Slide 22: Motor Power Circuit
TOP
FRONT
USB A
Receptacle
100 mA LED Lamp
Toggle Switch
USB
Solder
Controller
Mounting Plate
Nut
Screw
USB Micro-B
Receptacle
Motor Power
Cable Slot
Switch
Cutout
Controller

## Slide 23: Fiducial Mounting Plate
TOP
Screw, 6-32 × 3/8 in,
Flat Head, Zinc Plated (×4)
FRONT
Polycarbonate Sheet
203×254 mm (8×10 in)
⌀ 9/64 in, and
Counter Sink (×4)

## Slide 24: Fiducial Mounting Plate
TOP
Screw, 6-32 × 3/8 in,
Flat Head, Zinc Plated (×4)
Polycarbonate Sheet
203×254 mm (8×10 in)
⌀ 9/64 in, and
Counter Sink (×4)

## Slide 25: Software

## Slide 26: Software Architecture
Motor Driver Interface
Python
WiringPi
WiringPi2-Python
Pololu_drv8835_rpi
GPIO
Motor Driver
socket
USB
Wi-Fi

## Slide 27: Robot Control Network
Linksys
WRT54GL
192.168.2.1
192.168.2.100
Robot Control
Server
192.168.2.101:64000
Robot 1
192.168.2.102:64000
Robot 2
192.168.2.103:64000
Robot 3
192.168.2.104:64000
Robot 4

## Slide 28: Communication
Robot
Power
Process
Motor
Process
Control Server
Command: close
Terminate Process
Request Connection
Synchronize Timestamp
Query: batt
Battery Voltage
Supply Voltage in mV
Response: 0000
Accept Connection
and Send Timestamp
Request Connection
Accept Connection
Motor Command: 0,0
Motor Driver
Command: close
Terminate Process
Not Implemented

## Slide 29: Communication
Messages to Robot
Remote Access
  PuTTY
  Port 22 (0x16): Secure Shell (SSH)
  Start processes (for testing only?)
  Shutdown controller
Motor Command
  Port 64000 (0xFA00)
  Command: mL,mR
    Set left and right motor speeds
    Range: 0-1
  Command: close
    Terminate process
Battery Query
  Port 64160 (0xFAA0)
  Command: batt
    Request battery voltage
  Command: close
    Terminate process
Messages from Robot
Battery Response
  Port 64160 (0xFAA0)
  Data: 0000
    Battery voltage in mV
Not Implemented

## Slide 30: Robot API
Messages to Robot
Remote Access
  PuTTY
  Port 22 (0x16): Secure Shell (SSH)
  Start processes (for testing only?)
  Shutdown controller
Port 64000 (0xFA00)
Motor speed
command: mL,mR
mL <int> left motor
mR <int> right motor
integer value range:
max 100 full speed forward
0 stopped
min -100 full speed reverse
example:
100,100
Close robot client
close
Battery query
batt
Battery response
integer
battery voltage in mV
0000
Not Implemented
Not Implemented

## Slide 31: Motor Software Interface Options
Embed Python in C++ application
  http://stackoverflow.com/questions/22497532
  https://docs.python.org/2/extending/embedding.html
Use Python access to network services
  https://docs.python.org/3/library/socket.html#module-socket
  http://www.tutorialspoint.com/python/python_networking.htm



## Slide 32: Motor Software
DRV8835 Dual
Motor Driver Kit
for Raspberry Pi
GPIO
WiringPi
WiringPi2-Python
Pololu_drv8835_rpi
GPIO access library for the BCM2835 used in the Raspberry Pi
[GNU LGPLv3]
WiringPi version 2 implements functions for managing IO expanders
Python library for the Pololu DRV8835 Dual Motor Driver Kit for Raspberry Pi
Control Server
Motor Driver Interface
https://github.com/pololu/drv8835-motor-driver-rpi
Python application providing access via network socket
http://wiringpi.com/
https://github.com/Gadgetoid/WiringPi2-Python

## Slide 33: Software Build Guide

## Slide 34: Hardware
Raspberry Pi (RPi) 2 Model B
  https://www.raspberrypi.org/products/raspberry-pi-2-model-b/
Secure Digital (SD) memory card
  4 GB or larger
Edimax EW-7811Un USB Wi-Fi module
Pololu DRV8835 Dual Motor Driver Kit for Raspberry Pi
  https://www.pololu.com/product/2753
Peripherals (for software installation and configuration only)
  Monitor
    HDMI input or adapter (e.g., HDMI to DVI cable for monitor with DVI input
  USB keyboard
  USB mouse

## Slide 35: Operating System
Format SD card as FAT
  SD Formatter from SD Association
  https://www.sdcard.org/downloads/formatter_4/
Raspberry Pi (RPi) New Out Of the Box Software (NOOBS)
  https://www.raspberrypi.org/documentation/installation/noobs.md
  Download NOOBS and extract files
    https://www.raspberrypi.org/downloads/noobs/
  Copy extracted files to SD card (~20 minutes)
  Insert SD card into RPi
  Connect screen (HDMI), Ethernet (RJ45), Wi-Fi module, keyboard, and mouse
Install Raspbian
  Power on RPi
  Select install options
    OS Raspbian
    Language English (US)
    Keyboard us
  Click Install (~10 minutes)

## Slide 36: Configuration
Reboot:
~ $ sudo shutdown –r now
Configuration:
~ $ sudo raspi-config
Password: Follow on-screen instructions
Boot Option: B1 Console
Internationalisation
Locale: en_US.UTF-8 UTF-8
Default: en_US.UTF-8 UTF-8
Timezone: US, Eastern
Advanced Options: ..
A2 Hostname: e.g., rpi-2b-01
A4 SSH: Enabled
Reference:
https://www.raspberrypi.org/documentation/configuration/raspi-config.md

## Slide 37: Update Software
Update system packages:
~ $ sudo aptitude update
Update installed packages:
~ $ sudo aptitude upgrade
Update firmware:
~ $ sudo rpi-update

## Slide 38: Install Libraries
Download and install Python 3.
~ $ sudo aptitude install python3-dev python3-pip
Download and install WiringPi-Python.
~ $ sudo pip install wiringpi
Download and install Pololu_drv8835_rpi.
~ $ git clone https://github.com/pololu/drv8835-motor-driver-rpi.git
~ $ cd drv8835-motor-driver-rpi
~ $ sudo python setup.py install
Reference:
https://github.com/pololu/drv8835-motor-driver-rpi

## Slide 39: Wireless Configuration
Update interfaces configuration file before updating router DHCP routing list:
~ $ sudo nano /etc/network/interfaces
auto lo
iface lo inet loopback
iface eth0 inet manual
allow-hotplug wlan0
iface wlan0 inet manual
wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf
allow-hotplug wlan1
iface wlan0 inet manual
wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf
Reference:
https://www.raspberrypi.org/forums/viewtopic.php?f=28&t=50312

## Slide 40: Wireless Configuration
Update wpa_supplicant.conf configuration file:
~ $ sudo nano /etc/wpa_supplicant/wpa_supplicant.conf
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
country=GB
network={
ssid=“dd-wrt”
psk=“********”
proto=RSN
key_mgmt=WPA-PSK
pairwise=CCMP
group=CCMP
auth_alg=OPEN
}
network={
ssid=“WSU-ENG”
key_mgmt=NONE
}
Reboot:
~ $ sudo shutdown –r now

## Slide 41: Wireless Configuration
Update router DHCP routing list
  Status > LAN
  Copy MAC Address
  Services > Services
  Under DHCP Server
  Click Add
  Populate MAC Address, Host Name, and IP Address fields
  At the bottom of the page, click Apply Settings

## Slide 42: Wireless Configuration
Edit interfaces configuration file after updating router DHCP routing list:
~ $ sudo nano /etc/network/interfaces
auto lo
iface lo inet loopback
iface eth0 inet manual
allow-hotplug wlan0
#iface wlan0 inet manual
iface wlan0 inet dhcp
wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf
allow-hotplug wlan1
iface wlan0 inet manual
wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf
Reboot:
~ $ sudo shutdown –r now

## Slide 43: Software Installation
FileZilla
  File > Site manager
    Protocol SFTP
    Host IP address
    Port 22
    Logon Type Normal
    User pi
    Password cares
    Click Connect

## Slide 44: Launch Script
Create a launch script:
~ $ sudo nano launch-robot-1.sh
#!/bin/sh
# launch-robot-1.sh
echo `date +"%Y-%m-%d %H:%M:%S"` `hostname`
#sleep 20
cd /
cd /home/pi
echo `date +"%Y-%m-%d %H:%M:%S"` robot-client-1.py
sudo python3 robot-client-1.py $1
sudo shutdown –h now
Make script executable:
~ $ chmod 755 launch-robot-1.sh

## Slide 45: Schedule Script Task
Reboot:
~ $ sudo shutdown –r now
Execute command every boot | @reboot cmd
Redirect standard output to overwrite log file | cmd > logfile
Redirect standard output to append log file | cmd >> logfile
Redirect standard output and standard error | cmd >> logfile 2>&1
Schedule cron task:
~ $ sudo crontab -e
@reboot sh /home/pi/launch-robot-1.sh >/home/pi/log/cronlog 2>&1
Create log directory:
~ $ mkdir log
References:
https://help.ubuntu.com/community/CronHowto
http://www.instructables.com/id/Raspberry-Pi-Launch-Python-script-on-startup/
http://www.unixgeeks.org/security/newbie/unix/cron-1.html

## Slide 46: Raspberry Pi Cheat Sheet
Task | Command
Edit text file | nano ~/path/file sudo nano /path/file
Get IP address | hostname –I -or- ip addr
Update packages | sudo aptitude update sudo aptitude upgrade
Update firmware | sudo rpi-update
Hardware | Command
CPU information, including serial number | cat /proc/cpuinfo -also- lscpu
Memory | cat /proc/meminfo
Memory available | free –o -h
Disk partitions | cat /proc/partitions
Linux kernel version, distribution number, gcc version, etc. | cat /proc/version
List attached devices | lsusb
Environment | Command
Start graphical interface | startx
Reboot | sudo shutdown –r now -or- sudo reboot
Shutdown | sudo shutdown –h now -or- sudo halt
Processes | Command
Find process number | ps aux ¦ grep /path/script.py
Stop process no. 1984 | sudo kill 1984
Stop Python script | Ctrl + Shift + \

## Slide 47: Robot Information
Robot | Brand | Model | Serial # | Hostname | IP Address | User | Password
1 | Raspberry Pi | 2B | 00000000ff954578 | rpi-2b-01 | 192.168.2.101 | pi | cares
2 | Raspberry Pi | 2B | 000000000344931c | rpi-2b-02 | 192.168.2.102 | pi | cares
3 | Raspberry Pi | 2B | 000000001e245a0a | rpi-2b-03 | 192.168.2.103 | pi | cares
4 | Raspberry Pi | 2B | 0000000052c2172e | rpi-2b-04 | 192.168.2.104 | pi | cares
test | Raspberry Pi | B+ | 00000000e92a74ee | rpi-bp-01 | 192.168.2.*** | pi | cares

## Slide 48: Backup

## Slide 49: References
Pololu DRV8835 Dual Motor Driver Kit for Raspberry Pi B+
  https://www.pololu.com/product/2753
  P-MOSFET Reverse Polarity Protection
    http://myelectrons.com/mosfet-reversed-protection/
    http://hackaday.com/2011/12/06/reverse-voltage-protection-with-a-p-fet/
Raspberry Pi B+ GPIO pinout
  http://pi.gadgetoid.com/pinout

## Slide 50: Motor Driver PCB
3:1 scale
16.51 mm
(0.65 in)
43.18 mm
(1.7 in)
2.54 mm
(0.1 in)
2.54 mm
(0.1 in)
1.27 mm
(0.05 in)
5.08 mm
(0.2 in)
Pitch: 4.5-5.7 mm
5.67 mm
4.49 mm
5 mm

## Slide 51: Power and Motor Control
S7V7F5 switching 5V regulator with lab power supply at 7.2 V
  Idle: 200-230 mA
    Raspberry Pi B+, HDMI, keyboard, mouse, Wi-Fi, DRV8835 motor driver
Dagu Rover 5 platform with lab power supply at 7.2 V
  No track resistance: 350 mA
  With track resistance: 400 mA
    Platform moving on level surface
    1140 gram payload

## Slide 52: JST Connectors
VA Locking Header
VH Shrouded Header
VH Housing
B2P3-VH
B2P3S-VH
B3P-VH-FB-B
VHR-3N
Contact | Wire Size
SVH-21T-P1.1 | 18-22 AWG
SVH-41T-P1.1 | 16-20 AWG
Contact | Hole Size
1.14 mm Square Pin | 1.65 mm
Contact | Hole Size
1.14 mm Square Pin | 1.65 mm
VH Header |  |  | 
Circuits | Locking |  | Shrouded
 | Top Entry | Side Entry | Top Entry
3 | B3P-VH | B3PS-VH | B3P-VH-FB-B
6 | B6P-VH | B6PS-VH | B6P-VH-FB-B

## Slide 53: JST Connectors
NV Housing
Contact | Wire Size
SVH-21T-P1.1 | 18-22 AWG
SVH-41T-P1.1 | 16-20 AWG
XA Housing
Contact | Wire Size
SXA-001T-P0.6 | 22-28 AWG
SXA-01T-P0.6 | 20-24 AWG
SXA-001T-P0.6L | 22-26 AWG

## Slide 54: Robot
FRONT
REAR
1:2 SCALE

## Slide 55: Drawings
USB A plug
4
3
2
1
USB A receptacle
USB Micro-B
receptacle
breakout board
USB Micro-B plug
USB Micro-B receptacle
1
2
3
4
5
4
3
2
1
5
1
1
2
3
4
5
1
5
LED lamp

## Slide 56: References
Raspberry Pi Mounting Hole Positions and Template. http://www.raspberrypi-spy.co.uk/2012/11/raspberry-pi-mounting-hole-positions-and-template/

## Slide 57: Wi-Fi Troubleshooting
https://www.raspberrypi.org/forums/viewtopic.php?f=28&t=44044
1) Check whether the WiFi stick is being picked up at all
~ $ sudo lsusb
Bus 001 Device 002: ID 0424:9512 Standard Microsystems Corp.
Bus 001 Device 001: ID 1d6b:0002 Linux Foundation 2.0 root hub
Bus 001 Device 003: ID 0424:ec00 Standard Microsystems Corp.
Bus 001 Device 004: ID 7392:7811 Edimax Technology Co., Ltd EW-7811Un 802.11n Wireless Adapter [Realtek RTL8188CUS]
2) Check whether the modules loaded
~ $ sudo lsmod
Module Size Used by
snd_bcm2835 21149 0
snd_pcm 90778 1 snd_bcm2835
snd_seq 61097 0
snd_seq_device 7209 1 snd_seq
snd_timer 23007 2 snd_pcm,snd_seq
snd 66325 5 snd_bcm2835,snd_timer,snd_pcm,snd_seq,snd_seq_device
joydev 9766 0
evdev 11000 6
8192cu 569561 0
Uio_pdrv_genirq 3666 0
uio 9897 1 uio_pdrv_genirq

## Slide 58: Wi-Fi Troubleshooting
3) Check the WiFi NIC
~ $ ifconfig -a
wlan0 Link encap:Ethernet HWaddr 74:da:38:0a:21:22
UP BROADCAST MULTICAST MTU:1500 Metric:1
RX packets:0 errors:0 dropped:0 overruns:0 frame:0
TX packets:0 errors:0 dropped:0 overruns:0 carrier0
collisions:0 txqueuelen:1000
RX bytes:0 (0.0 B) TX bytes (0.0 B)
4) Check the WiFi configuration
~ $ cat /etc/network/interfaces
auto lo
iface lo inet loopback
eface eth0 inet dhcp
allow-hotplug wlan0
iface wlan0 inet manual
wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf
iface default inet dhcp