## Slide 1: Hardware

## Slide 2: Camera Mount
TOP
FRONT
Mount camera inside chassis?
24
?

## Slide 3: Camera Mount
REF: Camera PCB ~1 mm Thick
REF: Chassis Wall ~2-3 mm Thick
TOP
Pi NOIR Camera
Screw, M2-0.4 × 6 mm, Nylon (×8)
Standoff, M2-0.4 × 6 mm, Brass (×4)
FRONT
Guard to protect camera?
Mount camera inside chassis?
24
?

## Slide 4: Controller Mount
Raspberry Pi A+
Raspberry Pi B+
TOP
56
85
58
49
56
58
49
65
FRONT

## Slide 5: Controller Mount
TOP
Controller
Mounting Plate
170×90 mm
(6.7×3.5 in)
Material?
FRONT
? Office Depot black plastic clipboard 6”×9” (1 ea. $3.99)

## Slide 6: Camera Ribbon Cable
Insert ribbon cable with silver contacts toward HDMI connector
+
–

## Slide 7: Controller and Camera
Raspberry Pi B+
Pi NOIR Camera
56
85
58
49
4× M2.5 Mounting Holes
16.2
9.35
2
25
23.9
4× M2 Mounting Holes
PCB ~1 mm thick
6 mm from face of camera to reverse side of the PCB

## Slide 8: Robot
+
–
FRONT
REAR
1:2 SCALE

## Slide 9: Software

## Slide 10: Software Architecture
Motor Driver Interface
Application
Python
Language
WiringPi
WiringPi2-Python
Pololu_drv8835_rpi
Library
GPIO
Interface
Motor Driver
Hardware
socket
USB
Wi-Fi
Image Processing
CSI
Pi NoIR Camera
MMAL
bcm2835-v4l2
OpenCV-Python
OpenMax

## Slide 11: Image Processing Options
Video Capture
Video4Linux (V4L2) driver bcm2835-v412
  https://www.raspberrypi.org/forums/viewtopic.php?t=62364
  http://www.ics.com/blog/raspberry-pi-camera-module
  http://raspberrypi.stackexchange.com/questions/17068
  http://raspberrypi.stackexchange.com/questions/28003
  http://raspberrypi.stackexchange.com/questions/24262
  https://github.com/raspberrypi/linux/blob/rpi-3.10.y/Documentation/video4linux/bcm2835-v4l2.txt
  https://www.raspberrypi.org/forums/viewtopic.php?f=43&t=65026
RaspiCam
  raspistill
  raspivid
Picamera
  Pure Python interface to RPi Camera
Image Processing
OpenCV
  Python bindings / interface for OpenCV
  Real time image capture
  Image processing (brightness, contrast, thresholds, etc.)
  Object recognition (faces, bodies, etc.)
  Recognition of homogenous characteristics (blob)
SimpleCV
  Python
  Easy to use
Custom
  C/C++ or Python







## Slide 12: Camera Software
Pi NoIR Camera
CSI-2
Control Server
Image Processing
Python application providing access via network socket
Video4Linux (V4L2) driver
Broadcom Multi-Media Abstraction Layer
MMAL
bcm2835-v4l2
OpenMAX
Camera Serial Interface 2 Specification
OpenCV-Python
Library of OpenCV bindings
Open Media Acceleration
http://elinux.org/Rpi_Camera_Module
Fiducial marker detection and tracking coordinates

## Slide 13: Video4Linux (V4L2)
Load module:
sudo modprobe bcm2835-v4l2
Enumerate controls the driver exposes:
v4l2-ctl --list-ctrls
Take a picture to test:
v4l2-ctl --set-fmt-video=width=2592,height=1944,pixelformat=3
v4l2-ctl --stream-mmap=3 --stream-count=1 --stream-to=test1.jpg
Load module on boot:
sudo nano /etc/modules
bcm2835-v4l2
Flip image:
V4l2-ctl –-set-ctrl=vertical_flip=1
V4l2-ctl –c vertical_flip=1

## Slide 14: OpenCV-Python
Installation
  Install Cmake
  sudo apt-get update
  sudo apt-get install cmake
  Install OpenCV
  sudo apt-get update
  sudo apt-get install libopencv-dev
  sudo apt-get install pyton-opencv
Tutorials
  http://docs.opencv.org/master/d6/d00/tutorial_py_root.html
  http://docs.opencv.org/master/dd/d43/tutorial_py_video_display.html
  http://docs.opencv.org/master/d7/d4d/tutorial_py_thresholding.html
API documentation
  http://docs.opencv.org/modules/highgui/doc/reading_and_writing_images_and_video.html
  http://docs.opencv.org/modules/highgui/doc/user_interface.html

## Slide 15: OpenCV-Python
Import modules
import sys
import time
import cv2
Initialize video capture
device_index = 0 # assume only one camera connected
capture = cv2.VideoCapture(device_index) # create video capture object
time.sleep(1) # wait for initialization
capture.set(3, 640) # frame width
capture.set(4, 480) # frame height
Capture and process frames
while True:
ret,frame = capture.read() # grab and decode next video frame
gray = cv.cvtColor(frame, cv2.COLOR_BGR2GRAY) # grayscale convert
ret,thresh = cv2.threshold(gray,127,255,cv2.THRESH_BINARY) # threshold image
cv2.imshow("frame", thresh) # display image
if cv2.waitKey(1) & 0xFF == 27: # check if user pressed 'Esc' key
break
Free resources at exit
capture.release() # close capturing device
cv.destroyAllWindows() # close window and de-allocate associated memory

## Slide 16: Matrix Barcode Detection
Process a single image
  ~0.02 second (process image)
  ~0.03 second (process image, draw contours)
  ~0.05 second (process image, draw contours, print debug messages)
640×480 (VGA 4:3)
  13 fps (no processing)
  4 fps (CPU 43%)
  5 fps (CPU 54%)
  6 fps (CPU ~65%)
  7 fps (CPU ~75%, total CPU 100%)
480×270 (HVGA 16:9)
  7 fps (CPU 37%)
  10 fps (CPU 55%)
  15 fps (CPU 80%, total CPU 100%)
320×240 (QVGA 4:3)
  10 fps (CPU 38%)
  15 fps (CPU 58%)
  20 fps (CPU ~75%)
  ncurse

## Slide 17: AprilTags
Install dependencies for AprilTags
  sudo apt-get install subversion cmake libopencv-dev libeigen3-dev libv4l-dev
Check out AprilTags from the public svn repository
  svn co https://svn.csail.mit.edu/apriltags
The AprilTags library uses the pods build system in connection with cmake
  cd apriltags
  make
After compiling, run the example program
  ./build/bin/apriltags_demo
References
  Installation instructions: http://people.csail.mit.edu/kaess/apriltags/
  Main website: http://april.eecs.umich.edu/wiki/index.php/AprilTags

## Slide 18: Fiducial Marker Options
AprilTags
  apriltags_demo
  Raspberry Pi B+, 640×480: ~0.7 fps
  Raspberry Pi 2 B, 640×480, detecting 3 fiducials: ~2.5 fps (24% CPU)
  Raspberry Pi 2 B, 320×240, detecting 3 fiducials: ~8.5 fps (24% CPU)
Matrix Barcode
  Acceptable frame rate and detection reliability



## Slide 19: RaspiCam
Three command line driven applications comprise RaspiCam
  raspistill and raspistillyuv capture images
  raspivid captures video
RaspiCam takes advantage of Multi-Media Abstraction Layer (MMAL) API
  Broadcom specific API used only for Videocore 4 systems
  Runs over OpenMAX
Use up to four OpenMax (MMAL) components
  camera – used by all 3 applications
  encoder
    raspistill uses Image Encode component
    raspistillyuv does not use an encoder
    raspivid uses Video Encode component
  preview
    optionally used full screen or directed to specific rectangular area of the display
  null_sink
    “absorbs” preview frames if preview is disable

## Slide 20: Camera Software
RaspiCam
  raspberrypi\userland\host_applications\linux\apps\raspicam
Broadcom Host
  raspberrypi\userland\host_applications\linux\libs\bcm_host
Multi-Media Abstraction Layer (MMAL)
  raspberrypi\userland\interface\mmal
VideoCore OS Abstraction Layer (VCOS)
  raspberrypi\userland\interface\vcos

## Slide 21: Camera Software
Standard libraries
  <ctype>
  <stdio>
  <stdlib>
  <string>
  <memory>
BSD
  <sysexits.h>
POSIX
  <semaphore.h>
Broadcom
  bcm_host.h
Multi-Media Abstraction Layer (MMAL)
  interface/mmal/mmal.h
  interface/mmal/mmal_logging.h
  interface/mmal/mmal_buffer.h
  interface/mmal/util/mmal_util.h
  interface/mmal/util/mmal_util_params.h
  interface/mmal/util/mmal_default_components.h
  interface/mmal/util/mmal_connection.h
VideoCore OS Abstraction Layer
  interface/vcos/vcos.h
RaspiCam Dependencies